## Slide 1: ECSE 527 Design Project: MEMs-Based OCT Endoscope
Timothy Perrier
11/23/2020

## Slide 2: Background
Optical Coherence Tomography
Non-invasive and used for in-vivo imaging
Typically uses light from infrared range

## Slide 3: OCT Challenges
Very small image size
Difficult to image larger organs
Typically small scan angles
  10-20°
Short working distances

## Slide 4: Functionality
Used to produce cross-sectional images of bodily tissue
Can produce 2D or 3D images
Laser is scanned along a sample
Detector receives light reflected from sample
  Different tissue types reflect different intensities

## Slide 5: Example OCT Image and Analysis

## Slide 6: OCT System Overview
Input beam split into sample and reference
  Light coming back from both arms is recombined
Detector reads reflection intensity
Back-reflection from reference and sample arms interfere and gets converted into an image

## Slide 7: Design Specifications
Use an 830 nm light source
Achieve a field of view
Fit everything in a tube with a 7 mm diameter
Only design the beam delivery system

## Slide 8: Design Components and Tradeoffs
Used a C-Lens rather than GRIN
  Focal length was longer than using GRIN Lenses, but occupied much less space
Followed design from figure to the right
Mirror angled at 45˚ and tilts ±10° relative to X-plane
Mirror tilts ±10° relative to Y-plane
Tube diameter 7 mm
S. Luo et al., "A Miniature Endoscopic Optical Coherence Tomography Probe Based on C-Lens," in IEEE Photonics Journal, vol. 10, no. 5, pp. 1-10, Oct. 2018, Art no. 3901310, doi: 10.1109/JPHOT.2018.2870690.

## Slide 9: C-Lens Details
5 mm length
5 mm radius on curved side
1.78 refractive index (SF11 SCHOTT)
α angle 0 °
Collimates and focuses light source

## Slide 10: Design Overview
Beam (830 nm) is sent through a C-Lens
Mirror reflects beam through a window, onto the sample
C-Lens
Scanning Mirror
Window
Sample (ex: skin)

## Slide 11: Performance
Side view of the system with 5 different mirror positions
Maximum scan Length in this direction is approximately 6.4 mm
Scan length in the opposite direction is ~ 4.15 mm
Working distance ~5.15 mm

## Slide 12: Performance (cont.)
Resulting field of view
~6.4 mm
~4.15 mm
  Larger scan angle would be required for an increase

## Slide 13: Spot Size Performance
Spot diagram to the right is the spot size with the best resolution (45° tilt)
Spot diagram to the left is at 35° tilt
Low RMS values and small spot size

## Slide 14: Spot Size Performance (cont.)
Spot size with Beta angle tilt included
Left: Alpha 35°, Beta -10°

## Slide 15: Spot Size Performance (cont.)
Spot size with Beta angle tilt included
Left: Alpha 55°, Beta 10°

## Slide 16: Future Improvements
Increase of Beta scan angle to achieve 5 mm length
Improve transverse resolution
Fix decreasing resolution as scan moves away from the center angle

## Slide 17: References
Aumann S., Donner S., Fischer J., Müller F. (2019) Optical Coherence Tomography (OCT): Principle and Technical Realization. In: Bille J. (eds) High Resolution Imaging in Microscopy and Ophthalmology. Springer, Cham. https://doi.org/10.1007/978-3-030-16638-0_3
“Introduction to OCT.” OBEL, University of Western Australia, obel.ee.uwa.edu.au/research/fundamentals/introduction-oct/.
Popescu, D. P., Choo-Smith, L. P., Flueraru, C., Mao, Y., Chang, S., Disano, J., Sherif, S., & Sowa, M. G. (2011). Optical coherence tomography: fundamental principles, instrumental designs and biomedical applications. Biophysical reviews, 3(3), 155. https://doi.org/10.1007/s12551-011-0054-7
S. Luo et al., "A Miniature Endoscopic Optical Coherence Tomography Probe Based on C-Lens," in IEEE Photonics Journal, vol. 10, no. 5, pp. 1-10, Oct. 2018, Art no. 3901310, doi: 10.1109/JPHOT.2018.2870690.